Rays of Hope:  Propulsion lasers to get parts up, Microwaves to get energy down and the effect of large-scale deployment on CO2.

by Keith Henson, Co-Founder, L5 Society

Power satellites are the only currently known, long-term, scalable, possibly economical solution to displacing fossil fuels.  They collect sunlight in geosynchronous orbit (GEO), and transmit microwave energy to the ground to 10-km-diameter receiving antennas, known as rectennas.  The (tilted) GEO orbit is illuminated 99% of the time, eliminating the need for storage.  The rectennas can be sited (in most cases) within a few hundred km of loads, reducing the cost for long distance electrical transmission.

In space, without wind and gravity, the mass per average kW is expected to be around 5 kg, one percent of the mass of a typical solar power installation on Earth.

The problem, ever since they were patented in the late 1960s, is getting the cost to deliver even light power satellite parts to GEO down to where they make economic sense, i.e., cost less than electricity from coal.  There now seems to be a way using propulsion lasers in space to get the transport cost under $100/kg, the peak investment under $60 B and for someone to make a lot of money.  The economic model shows a ten-year return on investment of 500%.

(Fold?)

This is my fourth article for The Oil Drum.  Two of them examined power satellites, but were mostly on proposals to solve the big economic problem, the cost of transporting parts to orbit.  http://www.theoildrum.com/node/5485 http://www.theoildrum.com/node/7898

There were unsolved problems in the last article such as how to return the launch vehicle to its launching runway.

There has been a lot of attention on the CO2 rising over 400 ppm recently.  Some are advocating political action to halt the rise.  That's not likely to happen because uprooting the world's energy economy would do more damage (kill more people faster) than the climate changes expected due to the high CO2 levels.

Figure 1

However, something changed in the last few months.  It suddenly looks like a relatively modest cost project could get the entire human race off fossils fuels in 20 years.  That will take the background in this article and some time to get used to the concept.

Power satellites would (obviously) be adopted on a huge scale, if the cost of energy from them undercut fossil fuels.  Coal can be progressively displaced for making electricity if power from space were to be priced at 5 cents per kWh and reduced over the next ten years to 2 cents per kWh.  Synthetic hydrocarbon fuels would cost a dollar a gallon if the cost of power went down to 1 cent per kWh (a longer term prospect).

Economic Analysis of GEO Laser Propulsion

It's not hard to get the cost for 5kg/kW power sats down in this range if the cost of lifting parts to GEO can be reduced to $100/kg or less.  Solar power on earth ties up material in the range of 500 kg/kW(average).  Power plants built in space, where they get full time sunlight and are not subject to wind and gravity, allows a hundred to one materials reduction to 5 kg/kW and an energy payback time of under two months.  However, the cost of transporting even a greatly reduced mass to space is a big problem.  One hundred dollars per kg is a hundred to one cost reduction over the current of around $10,000 per kg paid to put communication satellites in GEO.

A two-orders-of-magnitude reduction in transport cost seems to be possible, but not using chemical energy (other than the first step where a Skylon type vehicle burns hydrogen with air for about 1/4 of the velocity to orbit).

Figure 2 Skylon in flight with cutaway of one engine showing the recently tested precoolers that drop ram hot air to -140 in 1/100th of a second.  From Reaction Engines with permission.

Beyond Skylon's air-breathing phase, it takes a 3 GW laser located in GEO to accelerate the vehicle for the last 6 km/s to orbit.  This would use a simple sheet of tubes on the wings to heat hydrogen to 2700 K.  The laser tracks the vehicle along the equator for ~4000 km.  The long acceleration path allows a ten-fold increase in payload compared to a straight-up launch from a ground laser.

The 2700 deg K temperature gives an exhaust velocity of 7500 m/s.  If you understand the rocket equation, the effect on payload of higher exhaust velocity will not surprise you.  The payload fraction to orbit goes up about 5 times.

Figure 3 Diagram by author.

A 30-ton second stage (carried in Skylon's payload bay) also uses laser-heated hydrogen to transport 20 tons three times per hour to GEO.  The second stages (72 per day) are scrapped at GEO for construction material for the power satellites, making the entire dry weight of the second stage into payload.

Figure 4 Diagram by author.

Since my last Oil Drum article in June 2011, I wrote a much longer technical article for the peer reviewed Journal of the British Interplanetary Society.  The (not yet published) article analyzed a variant, putting the lasers in GEO rather than shooting the laser beams from the ground to GEO and using bounce mirrors.  This solved several problems.  First, we get the Skylon back to its runway by going into orbit and coming down one or more orbits later.  We no longer have the PR problem of incinerating birds and bats flying through the beam.

Finally, we avoid the hard problem of sending a high power laser beam up through the murky atmosphere and expecting it to stay focused to a few meter spot after a trip out to GEO and back down to LEO.  This method also avoids the problem of a cloud moving into the beam path and causing a launch failure.

Lowering the Cost

The big problem with this scheme is powering the first laser in GEO.  The JBIS article described an elaborate multi-step bootstrap model that built a 25,000-ton power satellite in GEO to power the first propulsion laser.  The cost came in just short of $140 B and the financial breakeven took 12 years.

Early in April 2013, the model became obsolete because Steve Nixon (otherwise known in energy circles for advocating Mega-Chimney) made a suggestion that cut the cost model by $80 B and cut the financial breakeven to 8 years.  At $60 B (and 500% ROI in ten years), it may be within the capacity of western finance.

Figure 5 Cumulative profit and loss in millions of dollars based on 5 cents per kWh declining to 2 cents per kWh over ten years.  In this model, power satellites are sold to utility companies as they are produced at $3.5 B/GW for 5 cents/kWh and $1.4 B for 2 cents/kWh .  Peak investment is ~$60 B.  The spreadsheet is here.

If the western world cannot or will not finance this project, the Chinese can.  It's only twice the cost of the Three Gorges Dam (22 GW).  They asked the Indians to join them in building power satellites last November.

http://articles.timesofindia.indiatimes.com/2012-11-02/india/34877401_1_space-solar-power-space-collaboration-v-ponraj

Steve's idea was inspired; power the propulsion laser for a few months from a huge (10 km) 12-GW phased-array transmitter on the ground.  Reciprocity states that the path loss will be the same if you swap the transmitter and receiver antennas.  http://en.wikipedia.org/wiki/Antenna_%28radio%29#Reciprocity  The rectenna in space would be much smaller and lighter than a power satellite.  An unclassified NASA study from 1987, NASACR179558 indicates a 6-GW rectenna in space would mass less than 1,000 tons (160 gm/kW) http://www.nss.org/settlement/ssp/library/1987-NASACR179558-RectennaTechnologyProgram.pdf   

Even better, the rectenna, laser, tracking optics and heat sink can all be built and tested in LEO, much cheaper to access than GEO.  If we don't use robotics, we have man-centuries of experience working in LEO.  Then the propulsion laser can be sent to GEO using electric thrusters powered from the same rectenna that powers the laser.

A first pass estimate of the mass (rectenna, laser, optics, heat sink) came in at 8,000 tons, most of it in the heat sink for the laser plus 2000 tons of reaction mass.  That is about 20 times the mass of the ISS.  Moving it to GEO takes 21 hours of thrust (exhaust velocity of 20 km/s) for the delta V to get it there.  The high exhaust velocity reduces the reaction mass fraction to 20%.  Powered when in view of the ground station for ten percent of the time, it could make the trip in ~10 days.

This method for powering the 3 GW propulsion laser from the ground using microwaves would be used for months to a year depending on how many laser type Skylons were available.  After they bring up the factory and a power satellite to replace the power from the ground, the $12 B transmitter would be torn out and rebuilt as a rectenna.  (A shorter time of use than the cofferdams used to dewater the foundations for dams.)

Using a propulsion laser beam from GEO to equatorial LEO does require choreographing.  The operators (actually computers) need to shut the beam off for a few milliseconds while a satellite in a lower orbit passes through the beam path.  This should not appreciably affect the vehicle acceleration because of the thermal averaging of the hydrogen heater.

The 3 GW laser is sized to bring up 500,000 tons of parts per year, enough for 100 GW of power satellites, probably 20 at 5 GW each.

Is this proposal a realistic way to solve the energy problem and cap the rise in CO2?  At the 100 GW-per-year production level analyzed here, certainly not, it's far too small.

However, a project making large profits and with demand for 20 times that much new power per year (two TW) can grow and grow fast.

Figure 7, author

If 10% of the lift capacity is diverted into more propulsion lasers, the production of power satellites can double every year and that will get the human race off fossil fuels and stop the rise in CO2.  In the simple model used to generate Figure 7, the CO2 levels off by 22 years from the start.

At 2 TW per year, the cargo to space would be around 10 million tons per year.  At some point, the environmental impact of that much traffic into space may force the use of asteroids or lunar material (even though the exhaust only makes water).

Continuing production of power satellites beyond immediate human needs would provide the energy needed to capture and sequester CO2 to any level desired, especially if large amounts of synthetic fuel were already being made using cheap energy and CO2 from the atmosphere.

Figure 6.  In this unsophisticated model, the increase of Co2 is calculated as 0.5 ppm/quarter times (15 TW-installed power sat TW) / 15 TW.  Peak installation rate is 2 TW/year.  CO2 increase stops when 15 TW of SBSP has been emplaced.  The decline is based on active removal of CO2 by power in excess of 15 TW.

Technology Readiness

Is such a project realistic given the current state of engineering?  I think it is.  For example, the James Webb telescope mirror is big enough and accurate enough for the propulsion laser.  A 4-meter mirror (LAMP) was completed in 1989 and the technology was pushed into the 10-11 meter class.

Using lasers in space is well understood because the engineering was worked out from 1984 to 1993 as part of the Strategic Defense Initiative (SDI), known in the mainstream media, as "Star Wars."  http://www.bibliotecapleyades.net/ciencia/ciencia_laser01.htm

In regard to the other critical piece of technology, the Skylon rocket plane, Reaction Engines received a two-year grant from the UK government totaling 60 million pounds in late June 2013 to build a full-scale SABRE engine prototype.  http://www.sen.com/news/uk-pledges-fresh-support-for-revolutionary-space-engine.html

Military and Policy Issues

Unfortunately, I have an unsolved problem with this proposal as well.  It's not a technical, but a political problem.  Propulsion lasers are also weapons, game-changing weapons.  From GEO one of them can see and attack somewhat less than half the world.  Would the US accept China having one?  Would China accept the US having one?  Is joint control possible, perhaps including India, China, the US, Australia, Japan and Russia?  Can technical limits such as a laser wavelength that doesn't penetrate to the ground be built into the design?  Could the mechanical design prevent them from being pointed off the equatorial acceleration path?

A vast amount of detail has accumulated over the last year and a half.  If readers want to volunteer to comb through and nitpick spreadsheets and the assumptions that went into them, the project could use you.  If you find things to correct, my email is hkeithhenson@gmail.com   I could also use a contact to keep the US government informed if someone knows how to do that.

# Endnotes

Power is priced at 200 per kW (for the rectenna) plus a charge for the power satellite of 1400/kW to 3500/kW ($1.4 B to 3.5 B) divided by 80,000.  Thus, $1600/80,000 is 2 cents per kWh and  $3700/80,000 is 4.6 cents per kWh.  The factor of 80,000 is consistent with 6.8% discount and 20 years used in the US Energy Department's levelized cost analysis of new power sources.